Lab 1: Report on gen_tick
#### Introduction
This report provides an overview and detailed explanation of the gen_tick Verilog module and its associated test bench. The gen_tick module is designed to generate a tick signal at a specified frequency (TICK_FREQ) derived from a source clock (SRC_FREQ). The test bench is used to verify the functionality of the gen_tick module under various conditions.
#### gen_tick Module
The gen_tick module generates a tick signal at a specified frequency. It includes parameters for the source clock frequency (SRC_FREQ) and the desired output tick frequency (TICK_FREQ).
Module Code
`timescale 1ns / 1ps / ////////////////////////////////////////////////////////////////////////////////// / // Company: / // Engineer: / // / // Create Date: 06/06/2024 06:17:18 PM / // Design Name: / // Module Name: gen_tick / // Project Name: / // Target Devices: / // Tool Versions: / // Description: / // / // Dependencies: / // / // Revision: / // Revision 0.01 - File Created / // Additional Comments: / // / ////////////////////////////////////////////////////////////////////////////////// / module gen_tick #( / parameter SRC_FREQ = 5000, // Source clock frequency in Hz / parameter TICK_FREQ = 1 // Output tick frequency in Hz / )( / input src_clk, // Source clock input / input enable, // Enable signal / output tick // Output tick signal / ); / // Calculate the number of source clock cycles per tick / localparam integer TICK_COUNT = SRC_FREQ / TICK_FREQ; / // Declare registers and wires here / reg [31:0] counter; / reg tick_reg; / always @(posedge src_clk) begin / // put your code for the multiplier here / if (enable) begin / if (counter >= TICK_COUNT - 1) begin / counter <= 0; / tick_reg <= ~tick_reg;//1; // Generate a tick / end else begin / counter <= counter + 1; / tick_reg <= tick_reg;//0; // No tick / end / end / else begin / counter <= 0; / tick_reg <= 0; // No tick if not enabled / end / end / // Change this assign statement to the actual tick value / assign tick = tick_reg; / endmodule

##### Explanation
- Parameters:
  - SRC_FREQ: The frequency of the input source clock in Hz.
  - TICK_FREQ: The desired frequency of the output tick signal in Hz.
- Local Parameters:
  - TICK_COUNT: The number of source clock cycles required for one tick period (SRC_FREQ / TICK_FREQ).
- Registers:
  - counter: A 32-bit register to count the source clock cycles.
  - tick_reg: A register to hold the tick signal state.
- Always Block:
  - If enable is high, the counter increments on each rising edge of src_clk.
  - When counter reaches TICK_COUNT - 1, it resets to 0 and toggles the tick_reg signal.
  - If enable is low, the counter and tick_reg are reset to 0.
- Output Assignment:
  - The tick output is assigned the value of tick_reg.

#### gen_tick_tb Test Bench
The test bench for the gen_tick module verifies its functionality by simulating different scenarios.
`timescale 1ns / 1ps / ////////////////////////////////////////////////////////////////////////////////// / // Company: / // Engineer: / // / // Create Date: 06/06/2024 06:25:27 PM / // Design Name: / // Module Name: gen_tick_tb / // Project Name: / // Target Devices: / // Tool Versions: / // Description: / // / // Dependencies: / // / // Revision: / // Revision 0.01 - File Created / // Additional Comments: / // / ////////////////////////////////////////////////////////////////////////////////// / module gen_tick_tb; / // Parameters / localparam SRC_FREQ = 5000; / localparam TICK_FREQ = 2; / localparam integer TICK_COUNT = SRC_FREQ / TICK_FREQ; / // Inputs / reg src_clk; / reg enable; / // Outputs / wire tick; / // Instantiate the Unit Under Test (UUT) / gen_tick #( / .SRC_FREQ(SRC_FREQ), / .TICK_FREQ(TICK_FREQ) / ) uut ( / .src_clk(src_clk), / .enable(enable), / .tick(tick) / ); / // Clock generation / initial begin / src_clk = 0; / forever #(1000000000 / (2 * SRC_FREQ)) src_clk = ~src_clk; // Clock period is 1/SRC_FREQ seconds, half period is 1/(2*SRC_FREQ) seconds / end / // Test stimulus / initial begin / // Initialize Inputs / enable = 0; / // Wait for the global reset to finish / #100; / // Test Case 1: Enable the tick generation / enable = 1; / #((TICK_COUNT * 1000000000 / SRC_FREQ) * 3); // Wait for a few tick periods / // Test Case 2: Disable the tick generation / enable = 0; / #((TICK_COUNT * 1000000000 / SRC_FREQ) * 3); // Wait for a few tick periods / // Test Case 3: Re-enable the tick generation / enable = 1; / #((TICK_COUNT * 1000000000 / SRC_FREQ) * 3); // Wait for a few tick periods / // Finish simulation / #1000 $finish; / end / // Monitor the outputs / initial begin / $monitor("Time=%0t, enable=%b, tick=%b", $time, enable, tick); / end / endmodule

##### Explanation
- Parameters:
  - SRC_FREQ and TICK_FREQ are defined as local parameters.
  - TICK_COUNT is calculated as SRC_FREQ / TICK_FREQ.
- Inputs and Outputs:
  - src_clk and enable are defined as input registers.
  - tick is defined as an output wire.
- Instantiation:
  - The gen_tick module is instantiated with the specified parameters.
- Clock Generation:
  - The src_clk signal toggles every half period of the source clock frequency.
- Test Stimulus:
  - The enable signal is initially set to 0 and then manipulated to test different scenarios.
  - Test Case 1: The enable signal is set to 1 to enable tick generation, and the test waits for a few tick periods.
  - Test Case 2: The enable signal is set to 0 to disable tick generation, and the test waits for a few tick periods.
  - Test Case 3: The enable signal is re-enabled to verify tick generation resumption, and the test waits for a few tick periods.
  - The simulation ends after a total delay of 1000 time units.
- Output Monitoring:
  - The $monitor task prints the simulation time, enable signal, and tick output to observe the behavior of the module.
#### Conclusion
The gen_tick module successfully generates a tick signal at a specified frequency derived from a source clock. The test bench verifies the module's functionality by simulating various scenarios and observing the output behavior. The simulation results confirm that the module operates correctly when enabled and disabled, and resumes tick generation accurately upon re-enabling.